## Slide 1
How to change filters
AT
V
C
A
R
D
I
F
F
A
U
D
I
O
L
O
G
Y
T
E
A
M
T
I
M
A
W
D
I
O
L
E
G
C
A
E
R
D
Y
D
D
A
’
R
F
R
O
^
Audiology Clinic
Clinic 9, Outpatients
University Hospital of Wales
Heath Park Way
Cardiff
CF14 4xw
Tel: 029 218 43179
Mobile (Text Only): 07805 670 359
Email: Audiology.Helpline.CAV@Wales.nhs.uk
For a video guide, search on YouTube “Wax filter - Ambio RIE” or scan the QR code.
Step 1
Below are your wax guards, this has two functions, to remove your used filter and holds your new filter
Push the new wax guard onto the receiver (other end of the black stick). Push until the new guard is flush with the end of the receiver.
Remove your dome by pinching the end and pulling it off. Then insert the black end of the rod into the white wax guard. Pull this wax guard out.
Pull the black stick back out and the wax guard should remain on the hearing aid. The dome can now be placed back on the hearing aid.
Step 4
Step 3
Step 2
Notes: Colours (RGB):
Blue Text = 0 130 155
Turquoise Background = 170 219 207